CELLULAR ANTENNA TOWER REGULATIONS

LYON COUNTY KENTUCKY

THE PROPONENT FOR THESE REGULATIONS IS THE EDDYVILLE-KUTTAWA-LYON COUNTY JOINT PLANNING COMMISSION

APPROVED AND ADOPTED APRIL 18, 2011

I.	PURPOSE

The purposes of these regulations are as follows: to provide for the 	safest and most efficient integration of cellular antenna towers for 	cellular telecommunications services or personal communications 	services within all of Lyon County including the cities of Eddyville 	and Kuttawa; to provide for such families in coordination with the 	recommendations of the comprehensive plan; and to allow for such 		facilities with the intention of furthering the public health, safety, and 	general welfare.

II.	PRE-APPLICATION CONFERENCE

Applicants are encouraged to notify the planning commission to 	discuss proposals, allow for early coordination, and identify those 	items that are in conformance/nonconformance with the 	comprehensive plan, applicable zoning ordinances, and the provisions 	of these regulations.

III.	DEFINITIONS

For the purposes of these regulations, the following definitions shall 	apply:

A.	“Alternative Cellular Antenna Tower” means man-made trees, 			clock towers, bell towers, steeples, light poles, and similar 			alternative-design mounting structures that accommodate, 			camouflage, minimize or conceal the presence of cellular 				antennas or cellular antenna towers that are constructed 				primarily for the purpose of accommodating cellular antennas 			or cellular antenna towers or are reconstructed for the purpose 			of accommodating cellular antennas or cellular antenna towers.  		This does not include existing structures erected for another 			primary purpose, but which subsequently have cellular 				antennas attached to or located within them, without any 				reconstruction of the original structure.  For the provisions of 			these regulations, an alternative cellular antenna tower is 				considered a cellular antenna tower.

B.	“Antennas or Related Equipment” means transmitting, 				receiving, or other equipment used to support cellular 				telecommunications service or personal communications 				service.  This definition does not include towers.

C.	“Cellular Antenna Tower” means a tower constructed for, or 			an existing facility that has been adapted for, the locations of 			transmission or related equipment to be used in the provision of 		cellular telecommunications services or personal 					communications services.

D.	“Cellular Telecommunications Service” means a retail 				telecommunications service that uses radio signals transmitted 			through cell sites and mobile switching stations.

E.	“Co-location” means locating two (2) or more transmission 			antennas or related equipment on the same cellular antenna 			tower.

F.	“Guyed Cellular Antenna Tower” means a type of wireless 			transmission tower that is supported by thin guy wires.

G.	“Lattice Cellular Antenna Tower” means a self-supporting 			tower with multiple legs and cross-bracing of structural steel.

H.	“Monopole Cellular Antenna Tower” means a slender self-			supporting tower on which wireless antennas can be placed.

I.	“Personal Communication Service” has the meaning as 				defined in 47 U.S.C. sec.332 ©.

J.	“Planning Commission” means the Eddyville-Kuttawa-Lyon 			County Joint Planning Commission.

K.	“Uniform Application” means an application to construct a 			cellular antenna tower submitted to a planning commission in 			conformity with KRS 100.985 through KRS 100.987.

L.	“Utility” has the meaning as defined in KRS 278.010(3).

IV.	GENERAL

Cellular antenna towers for cellular telecommunications services or 	personal communications services may be allowed in any zone as a 	Conditional Use after a planning commission review in accordance 	with the following procedures to ascertain agreement with the 	adopted comprehensive plan and the regulations contained within the 	applicable zoning ordinance of the city of Eddyville or Kuttawa.

A.	Applicability

Every utility, or a company that is engaged in the business of 			providing the required infrastructure to a utility, that proposes 			to construct a cellular antenna tower shall submit a completed 			uniform application to the planning commission.  Where the 			planning commission finds that circumstances or conditions 			relating to the application of an alternative cellular antenna 			tower are such that one or more of the requirements of the 			uniform application listed below are not necessary or desirable 			for the protection of surrounding property or the public health, 			safety, and general welfare, and that such special conditions or 			circumstances make one or more said requirements 				unreasonable, the planning commission, or its duly authorized 			representative, may modify or waive such requirement of the 			uniform application, either permanently or on a temporary 			basis.  Any such modification or waiver shall be requested by 			the applicant, and the applicant shall submit a written 				justification for each request modification or waiver.

B.	Application Requirements

Applications for the construction of cellular antenna towers for 			cellular telecommunications services or personal 					communications services shall include the following:

1.	The full name and address of the applicant.

2.	The applicant’s articles of incorporation, if applicable.

3.	A copy of all permits and/or licenses issued by the Federal Communication Commission for the operation of the proposed tower in Lyon County.

4.	A geotechnical investigation report signed and sealed by a professional engineer registered in Kentucky that includes boring logs and foundation design recommendations.

5.	A written report, prepared by a professional engineer or 				land surveyor, of findings as to the proximity of the 				proposed site to flood hazard areas.

6.	Clear directions to the proposed site, including highway 				numbers and street names, if applicable, with the 					telephone number of the person who prepared the 					directions.

7.	The lease or sale agreement for the property on which 				the tower is proposed to be located, except that, if the 				agreement has been filed in abbreviated form with the 				County Clerk, an applicant may file a copy of the 					agreement as recorded by the County Clerk and, if 					applicable, the portion of the agreement that specifies, in 				the case of abandonment, a method that the utility will 				follow in dismantling and removing the proposed 					cellular antenna tower including a timetable for removal.

8.	The identity and qualifications of each person directly 				responsible for the design and construction of the 					proposed tower.

9.	A site development plan, signed and sealed by a 					professional engineer or surveyor licensed in Kentucky, 				that shows the proposed location of the tower and all 				easements and existing structures within five hundred 				(500) feet of the proposed site on the property on which 				the tower will be located, and all easements and existing 				structures within two hundred (200) feet of the access 				drive, including the intersection with the public street 				system.

10.	A survey, prepared by a surveyor licensed in Kentucky.  				The survey shall be in accordance with all of the 					requirements of the KRS 100, that shows lease lines or 				property lines, which upon approval, shall be recorded.

11.	A vertical profile sketch of the tower, signed and sealed 				by a professional engineer registered in Kentucky, 					indicating the height of the tower and the placement of 				all antennas.

12.	The tower and foundation design plans and a description 				of the standard according to which the tower was 					designed, signed and sealed by a professional engineer 				registered in Kentucky.

13.	A map, drawn to a scale no less than one (1) inch equals 				two hundred (200) feet, that identifies every structure 				and every owner of real estate within five hundred (500) 				feet of the proposed tower.

14.	A statement that every person who, according to the 				records of the property valuation administrator, owns 				property within five hundred (500) feet of the proposed 				tower or property contiguous to the site upon which the 				tower is proposed to be constructed, has been:

a.)	Notified by certified mail, return receipt requested, 				of the proposed construction which notice shall 					include a map of the location of the proposed 					construction.

b.)	Given the telephone number and address of the 					local planning commission

c.)	Informed of his or her right to participate in the 					planning commission’s proceedings on the 						application.

15.	A list of the property owners who received the notice, 				together with copies of the certified letters sent to the 				listed property owners.

16.	A statement that the Judge-Executive of Lyon County 				has been notified, in writing, of the proposed 					construction and given a copy of the notification.

17.	A statement that the Mayors of Eddyville and Kuttawa 				have been notified, in writing, of the proposed 					construction and given a copy of the notification.

18.	A statement that:

a.)	A written notice, on durable maternal at least two 					(2) feet by four (4) feet in size, stating that “[Name 				of applicant] proposes to construct a 							telecommunications tower on this site” and 						including the addresses and telephone numbers of 					the applicant and the planning commission, has 					been posted in a visible location on the proposed 					site.

b.)	A written notice, at least two (2) feet by four (4) 					feet in size, stating that “[Name of applicant] 					proposes to construct a telecommunications tower 					near this site” and including the addresses and 					telephone numbers of the applicant and the 						planning commission, has been posted on the 					public road nearest the site.

19.	A statement that notice of the location of the proposed 				construction has been published in the Herald Ledger 				newspaper.

20.	A brief description of the character of the general area in 				which the tower is proposed to be constructed, which 				includes the existing land use for the specific property 				involved.

21.	A statement that the applicant has considered the likely 				effects of the installation on nearby land uses and values 				and has concluded that there is no more suitable location 				reasonably available from which adequate service to the 				area can be provided, and that there is no reasonably 				available opportunity to locate its antennas and related 				facilities on an existing structure, including 						documentation of attempts to locate its antennas and 				related facilities on an existing structure, if any, with 				supporting radio frequency analysis, where applicable, 				and a statement indicating that the applicant attempted to 				located its antennas and related facilities on a tower 				designed to host multiple wireless service providers’ 				facilities or on an existing structure, such as a 					telecommunications tower or other suitable structure 				capable of supporting the applicant’s antennas and 					related facilities.

22.	A map of the area in which the tower is proposed to be 				located, that is drawn to scale, and that clearly depicts 				the necessary search area within which an antenna tower 				should, pursuant to radio frequency requirements, be 				located.

23.	A grid map that shows the location of all existing cellular 			antenna towers and that indicates the general position of 				proposed construction sites for new cellular antenna 				towers within an area that includes:

a.)	All of Lyon County; and

b.)	A one-half (½) mile area outside the boundaries of 					Lyon County, if that area contains either existing 					or proposed construction sites for cellular antenna 					towers.

V.	CONFIDENTIALITY OF APPLICATION

All information contained in the application and any updates, except 		for any map or other information that specifically identifies the 	proposed location of the cellular tower then being reviewed, shall be 	deemed confidential and proprietary within the meaning of KRS 	61.878.  The planning commission shall deny any public request for 	the inspection of this information, whether submitted under 	Kentucky’s Open Records Act or otherwise, except when ordered to 	release the information by a court of competent jurisdiction.  Any 	person violating this subsection shall be guilty of official misconduct 	in the second degree as provided under KRS 522.030.  The 	confidentiality of the applications and any updates of the application 	can be waived by the written authorization of the applicant.

VI.	APPLICATION FEE

An applicant for the construction of cellular antenna towers for 	cellular telecommunications services or personal communications 	services shall pay an application fee in the amount set by the 	planning commission upon submission of a uniform application.

VII.	PROCESSING OF APPLICATION

Applications for the construction of cellular antenna towers for 	cellular telecommunications services or personal communications 	services shall be processed as follows:

A.	At least one (1) public hearing on the proposal shall be held, at 			which hearing interested parties and citizens shall have the 			opportunity to be heard.  Notice of the time and place of such 			hearing shall be published at least once, in the Herald Ledger 			newspaper, provided that one (1) publication occurs not less 			than seven (7) calendar days nor more than twenty-one (21) 			calendar days before the occurrence of such hearing.

B.	Notice of the proposal shall be posted on the site at least 				fourteen (14) days in advance of the hearing.  The notice shall 			consist of a written notice, on durable material at least two (2) 			feet by four (4) feet in size, stating that “[Name of applicant] 			proposes to construct a telecommunications tower on this site” 			and including the addresses and telephone numbers of the 			applicant and the planning commission.  Notice of the proposal 			shall also be posted on the public road nearest the site.  This 			notice shall consist of a written notice, on durable material at 			least two (2) feet by four (4) feet in size, stating that “[Name of 			applicant] proposes to construct a telecommunications tower 			near this site” and including the addresses and telephone 				numbers of the applicant and the planning commission.

C.	Notice of the hearing shall be given at least fourteen (14) days 			in advance of the hearing, by certified mail, return receipt 			requested, to the owner of every parcel of property within five 			hundred (500) feet of the proposed tower or property 				contiguous to the site upon which the tower is proposed to be 			constructed.  The notice shall include a map of the location of 			the proposed construction, the telephone number and address of 		the planning commission, and shall inform the addressee of his 			or her right to participate in the planning commission’s 				proceedings on the application.  Records maintained by the 			property valuation administrator may be relied upon 				conclusively to determine the identity and address of said 			owner.  In the event a property is in condominium or				cooperative forms of ownership, then the person notified by 			mail shall be the president or chairperson of the owner group 			that administers property commonly owned by the 					condominium or cooperative owners.  A joint notice may be 			mailed to two (2) or more co-owners of an adjoining property 			who are listed in the property valuation administrator’s records 			as having the same address.

D.	Upon holding the hearing, the planning commission shall, 			within sixty (60) days commencing from the date that the 			application is received by the planning commission, or within a 			date specified in a written agreement between the planning 			commission and the applicant, make its final decision to 				approve or disapprove the uniform application.  If the planning 			commission fails to issue a final decision within sixty (60) 			days, and if there is no written agreement between the planning 			commission and the utility to a specific date of the planning 			commission to issue a decision, it shall be presumed that the 			planning commission has approved the utility’s uniform 				application.

VIII.	DESIGN STANDARDS

The applicant shall provide information demonstrating compliance 	with the requirements contained herein.  Potential sites that should be 	considered (in order from most-preferred to least-preferred) include 	existing utility towers, industrial zones, commercial zones, and 	government buildings and properties.  Where the planning 	commission finds that circumstances or conditions relating to the 	particular application are such that one (1) or more of the 	requirements listed below are not necessary or desirable for the 	protection of the surrounding property or the public health, safety, 	and general welfare, and that such special conditions or 	circumstances make one (1) or more said requirements unreasonable, 	the planning commission, or its duly authorized representative, may 	modify or waive such requirement, either permanently or on a 	temporary basis.  Any such modification or waiver shall be requested 	by the applicant, and the applicant shall submit a written justification 	for each requested modification or waiver.

A.	Monopoles

Monopole cellular antenna towers shall be permitted in any 			zone.  Lattice and Guyed cellular antenna towers shall be 				permitted in any zone except for Residential zones.

B.	Minimum Lot Size

Regardless of the minimum lot sizes listed in the specific 				zoning districts, or the Eddyville-Kuttawa-Lyon County 				Subdivision Regulations, the lot size may be the minimum 			necessary to comply with the objectives and standards of this 			section.

C.	Agricultural Zone Setback

Lattice and Guyed cellular antenna towers constructed in an 			agricultural zone shall be located a minimum distance of not 			less than two hundred fifty (250) feet from all existing 				residential structures.  Distance shall be measured from the 			base of the tower to the nearest wall of the residential structure.

D.	Setbacks

Setbacks for all structures constructed in connection with 			Guyed or Lattice cellular antenna towers, except fences and/or 			guy wires, shall be a minimum distance from the property line 			or lease line equal to at least one-half (½) the height of the 			tower, but not less than fifty (50) feet.  All structures 				constructed in connection with Monopole or Alternative 				cellular antenna towers shall comply with the applicable 				setback requirements established for other structures within the 			applicable zoning district.  Alternative cellular antenna towers 			that are to be located as part of a utility service facility (e.g. 			power pole or telephone pole) shall comply with setback 				requirements applicable to such utility service facilities, if any.

E.	Height

A cellular antenna tower, or alternative antenna tower structure, 			may be constructed to a maximum height of two hundred (200) 			feet regardless of the maximum height requirements listed in 			the specific zoning district.  This also applies to any tower 			taller that fifteen (15) feet constructed on the top of another 			building or structure, with the height being the overall height of 		the building/structure and tower together, measured from the 			grade to the highest point.   The planning commission may 			allow antennas greater than two hundred (200) feet in height 			upon review of the applicant’s justification.

F.	Construction Standards

The cellular antenna tower shall be constructed in compliance 			with the current ANSI/EIA/TIA 222-F standard and other 			applicable state standards.

G.	Illumination

Cellular antenna towers shall not be illuminated, except in 			accordance with other state or federal regulations.

H.	Staffing

The site shall be un-staffed.  Personnel may periodically visit 			the site for maintenance, equipment modification, or repairs.  			To accommodate such visits, ingress/egress shall be only from 			approved access points.

I.	Fencing

Woven wire or chain link (eighty (80) percent open) or solid 			fences made from wood or other materials (less than fifty (50) 			percent open) shall be used to enclose the site.  Such fences 			shall not be more than eight (8) feet in height, and may be 			located within the front, side, or rear yard.

J.	Screening

Screening shall be provided by evergreen trees, with a 				maximum height of six (6) feet, planted in a staggered pattern 			at a maximum distance of fifteen (15) feet on center.  The 			screening shall be placed in an area between the property line, 			or lease line, and a ten (10) foot setback.

K.	Surfacing

All driveways and off-street parking areas shall be paved with a 		durable surface such as asphalt or concrete.

L.	Signs

There shall be no signs permitted, except those displaying 			emergency information, owner contact information, warning or 			safety instructions, or signs that are required by a federal, state, 			or local agency.  Such signs shall not exceed five (5) square 			feet in area.

M.	Number of Service Providers

All new cellular antenna towers shall be designed and 				constructed to accommodate a minimum of three (3) service 			providers.

N.	Lease Agreements

All option and site lease agreements shall not prohibit the 			possibility of co-location, and in the case of abandonment, shall 		include a method that the utility will follow in dismantling and 			removing the proposed cellular antenna tower including a 			timetable for removal.

O.	Discontinuance of Use

If the use of any cellular antenna or cellular antenna tower or 			alternative cellular antenna tower structure is discontinued, the 			owner shall provide the planning commission with a copy of 			the notice to the FCC of intent to cease operations within thirty 			(30) days of such notice to the FCC.  If the cellular antenna or 			cellular antenna tower or alternative cellular antenna tower 			structure will not be reused, the owner shall have one hundred 			eighty (180) days from submittal of the FCC notice to the 			planning commission to obtain a demolition permit and remove 			the antenna or tower that will not be reused.  If the cellular 			antenna or cellular antenna tower or alternative cellular antenna 		tower structure is to be reused, the owner shall have no more 			than twelve (12) months from submittal of the FCC notice to 			the planning commission in which to commence new operation 			of the antenna or tower to be reused.  Upon failure to 				commence new operation of the antenna or tower that is to be 			reused within twelve (12) months, the cellular antenna or 				cellular antenna tower or alternative cellular antenna tower 			structure shall be presumed abandoned, and the owner shall 			obtain within ninety (90) days of the expiration of the twelve 			(12) month period, a demolition permit and remove the antenna 			or tower that is presumed abandoned within sixty (60) days of 			obtaining the demolition permit.  If the owner fails to remove 			an antenna or tower in the time provided by this paragraph, the 			planning commission may, on grounds of public safety, health, 			and welfare, cause the demolition and removal of the antenna 			or tower and recover its costs of demolition and removal.  The 			planning commission, at the time of application for 				construction, may require posting of a bond covering the cost 			of removal of the antenna or tower; the bond to be forfeited to 			the planning commission upon failure to remove the antenna or 			tower in a timely manner as required above.

P.	Existing Telecommunications Facilities

Telecommunications facilities in existence on the date of the 			adoption of these regulations which do not comply with these 			regulations are subject to the following provisions.  Owners of 			existing telecommunications facilities located in Lyon County 			will be required to submit the following documentation to the 			Planning Commission within six (6) months of the adoption of 			these regulations.

1.	A plat map drawn by a licensed engineer/surveyor 					showing the location of all structures associated with the 				facility; the height of the tower and its fall radius; the 				location of all buildings within the fall radius; the owner 				of the land on which the facility is located; the street 				address and GPS coordinate of the facility.

2.	Proof of liability insurance to cover the loss to others 				should the tower fall.

3.	A copy of the FCC approval and permits issued for the 				facility.

4.	Statement of understanding and expressed willingness to 				comply with the provisions of section VII-O 					(Discontinuance of Use) above.

5.	Statement as to the number of current users of the facility 			and the capacity of the tower to handle additional 					antennas.

6.	Existing telecommunications facilities may continue in 				use for the purpose now used, but may not be expanded 				or replaced without complying with these regulations, 				except as further provided in this section.

7.	Existing telecommunications facilities which are 					hereafter damaged or destroyed due to any reason or 				cause may be repaired and restored to their former use, 				location and physical dimensions subject to obtaining a 				building permit therefore, but without otherwise 					complying with this ordinance.

8.	The owner of any existing telecommunications facility 				may replace, repair, rebuild and/or expand such 					telecommunications facility to accommodate co-located 				antennas or facilities, or to upgrade the facilities to 					current engineering, technological or communications 				standards by obtaining a building permit therefore, and 				without having to conform to the provisions of this 				ordinance, including but not limited to, provisions of this 				ordinance regarding notice to local zoning authorities or 				posting of signs, or to otherwise request local zoning 				approvals, so long as such facilities are not increased in 				height and or setbacks are not decreased.

9.	Any such replacement, repair, reconstruction, or 					enlargement shall not violate the design standards 					described above beyond that existing at the date of the 				adoption of this ordinance.

Q.	Other Approvals Required

Approval of the Federal Aviation Administration (FAA) and the 			Kentucky Airport Zoning Commission (KAZC) or 					documentation where approval is not required shall be 				submitted prior to the issuance of a building permit for the 			construction of the cellular antenna tower.

IX.	CRITERIA

A.	Approval or Disapproval

The Planning Commission’s approval or disapproval of the 			proposal shall be based upon an evaluation of the proposal’s 			agreement with the comprehensive plan and zoning regulations.

1.	The planning commission may require the applicant to 				make a reasonable attempt to co-locate additional 					transmitting or related equipment.  The Planning 					Commission may provide the location of existing 					cellular antenna towers on which the commission deems 				the applicant can successfully co-locate its transmitting 				and related equipment.  If the Planning Commission 				requires the applicant to attempt co-location, the 					applicant shall provide the Planning Commission with a 				statement indicating that the applicant has:

a.)	Successfully attempted to co-locate on towers 					designed to host multiple wireless service 						providers’ facilities or existing structures such as a 					telecommunications tower or another suitable 					structure capable of supporting the applicant’s 					facilities, and that identifies the location of the 					tower or suitable structure on which the applicant 					will co-locate its transmission and related 						facilities; or

b.)	Unsuccessfully attempted to co-locate on towers 					designed to host multiple wireless service 						providers’ facilities or existing structure such as a 					telecommunications tower or another suitable 					structure capable of supporting the applicant’s 					facilities and that:

1.	Identifies the location of the towers or other 						structures on which the applicant attempted 						to co-locate; and

2.	Lists the reasons why the co-location was 						unsuccessful in each instance.

2.	The Planning Commission may deny a uniform 					application to construct a cellular antenna tower based 				on an applicant’s unwillingness to attempt to co-locate 				additional transmitting or related equipment on any new 				or existing towers or other structures.

3.	The Planning Commission shall not regulate the 					placement of a cellular antenna tower on the basis of the 				environmental effects of radio frequency emissions to the 			extent that the proposed facility complies with the 					regulations of the Federal Communications Commission 				concerning radio frequency emissions.

X.	AMENDMENTS

Any amendments to plans, except for minor adjustments as 		determined by the Planning Commission, or its duly authorized 	representative, shall be made in accordance with the procedure 	required by Section IV, subject to the same limitations and 	requirements as those under which such plans were originally 	approved.